## Slide 1
Danh-Tai HOANG,
“Design Principles of Cellular Networks” Group,
Asia Pacific Center for Theoretical Physics (APCTP),
Pohang, KOREA
March 27, 2014
Group Meeting
CUDA Fortran
Notes: 1

## Slide 2
GPU Architecture
- Compute capatibility: 2.0
- Number of multiprocessors: 14 ( 14 CPU)
- Number of cores: 448 (14 x 32)
Tesla C2075:
Notes: 2

## Slide 3
Execution Model
- Each kernel is launched in one grid.
- Maximum number of kernel: 16
* Host = CPU
* Device = GPU
* Kernel = function called from the host that runs on the device
- One kernel is executed at a time
- Many threads execute each kernel
CUDA programming
Notes: 3

## Slide 4
1. Registers
- Small
- Fast
2. Shared Memory
- Shared among threads in a single block
On-chip, small, as fast as registers
3. Global Memory
- Kernel input and output data reside here
- Off-chip (host), large
- Shared by all threads
- Inter-Grid communication
- Inter-Kernel sychronization.
* Host can read & write global memory but not shared memory.
* Threads within a block can:
+ communicate very quickly (shared memory)
+ Synchronize (wait for all threads to catch up)
* Threads in different block cannot cooperate
Notes: 4

## Slide 5
Thread ID – Block ID
+ threadIdx.x  thread ID within block
+ blockIdx.x  block ID within grid
+ blockDim.x  number of threads/block
+ gridDim.x  number of blocks/grid
Notes: 5

## Slide 6
Important Numbers
- Compute capatibility: 2.0
- Number of multiprocessors: 14
- Number of cores: 448 (= 14 x 32)
- Maximum number of resident blocks / multiprocessor: 8
- Maximum number of resident warps / multiprocessor: 48
- Maximum number of resident threads / multiprocessor: 1536
- Number of 32-bit registers / multiprocessor: 32 KB
- Maximum number of 32-bit registers / thread: 63
- Shared memory size / multiprocessor: 48 KB
- Constant memory size / multiprocessor: 64 KB
- Maximum Threads / Block: 1024
- Maximum Block Dimensions: 1024 x 1024 x 64
- Maximum Grid Dimensions: 65535 x 65535 x 65535 (231-1)
 All blocks may be not resident at the same time.
Notes: 6

## Slide 7
Optimizing
- Keep the multiprocessors on the device as busy as possible.
- The number of blocks in a grid should be larger than the number of multiprocessors so that all multiprocessors have at least one block to execute.
# blocks = 14 x const
- Threads per block should be a multiple of warp size (32)
# threads = 32 x const
128 ≤ # threads ≤ 256
Notes: 7

## Slide 8
Examples
ex1.f90
ex1.cuf
Notes: 8

## Slide 9
ex2.cuf
Notes: 9

## Slide 10
ex3.f90
ex3.cuf
Multidimensional arrays
Notes: 10

## Slide 11
Shared memory and Synchronization
ex4.cuf
Notes: 11